| Altimeter and statics system test in accordance with LTH 40 in agreement with FAR part 43 App.E and F | Form 40.3 | REGISTRATION: Characteristic: |
| --- | --- | --- |
|  | REVISION Revision 0 | AIRCRAFT TYPE: SERIAL No.: |
|  |  | Project No.: |
|  | Page 1 of 1 | DATE: Date: |
| 1. General information Place of execution Field altitude ft Airfield information ALt. No.1 stby Alt. No.2 QFE: QNH: Tolerance +/- 20 ft Altimeter S/N 2. Statics system leak test A) without pressurized cabin: Diff. Pressure at the altimeter 1000 ft over QFE b) with pressurized cabin: Altimeter at the max. Kabinendiff.- pressure over QFE Used max. Cabin Alt: MAX. pressure drop after 1min 100 ft Nr.1 Ind: Nr.2 Ind: 3. Scale error Checkpoints lndication in ft Tolerance Encoder in ft No.1 stby No.2 +/- ft +/- 125 ft - 1000 20 0 20 500 20 1000 20 1500 25 2000 30 3000 30 4000 35 4100 Encoder with Gilham Code only 8000 60 10000 80 12000 90 14000 100 15700 Encoder with Gilham Code only 16000 110 18000 120 20000 130 22000 140 25000 155 30000 180 31000 Encoder with Gilham Code only 35000 205 40000 230 45000 255 50000 280 4. Hysteresis test Alt 1 stby Alt2 Tol ft Housing leak test: At 18000 ft max. 100 ft/min - 100 Testpoint 1 50% max. Alt +/- 75 Testpoint 2 40% max. Alt +/- 75 Elast. effect. with daily pressure +/- 30 5. Barometric scale errors Pressure Pressure Altitude. in ft Indicator Toler. +/- 25 ft inch of Hg hPa for inHg for hPa No.1 stby No.2 28,10 952 - 1727 - 1715 28,50 965 - 1340 - 1334 29,00 982 - 863 - 864 29,50 999 - 392 - 391 29,92 1013 0 0 30,50 1033 531 531 30,90 1046 893 883 30,99 1050 974 989 6. Friction (750/min ft) Checkpoints lndication in ft Tolerance in ft No.1 stby No.2 +/- ft 1000 70 2000 70 3000 70 5000 70 10000 80 15000 90 20000 100 25000 120 30000 140 35000 160 40000 180 50000 250 7. Conclusion: All lines connected/original state Mechanic.: Insp.: Stamp Air DATA test set information Manufacturer: Model: Serial NUMBER: DATE OF Calibration: Accuracy Specification: |