| MODE S TRANSPONDER TESTREPORT | Formblatt 40.2 B | REGISTRATION: Kennzeichen: |
| --- | --- | --- |
|  | REVISION Revision 0 | AIRCRAFT TYPE: SERIAL-No.: |
|  | Seite 1 von 4 | PROJECT-No.: |
| Performed by: |  | DATE: Datum: |
| afa . Units under test #1 #2 Testset Manufacturer Manufacturer Type Type Partnumber Serial Number Serial Number Calibration Mod Status Elementary Surveillance capable Enhanced Surveillance capable Results Tests #1 #2 Tolerance Remarks Transmitterfrequency Mhz Mhz 1090 ±1 Mhz Sensitivity (MTL) lower Antenna dBm dBm -73 ±4 dBm upper Antenna dBm dBm -73 ±4 dBm Power lower Antenna dBm dBm 48,5< ERP <57,0 upper Antenna dBm dBm 48,5< ERP <57,0 SLS XPDR Reply SLS 0dB % % max. 1% SLS –9dB % % min. 90% Mode S address _____________ _____________ Transponder must not reply to any other than its assigned address ○ pass ○ fail ○ pass ○ fail Mode S diversity Isolation dB dB >20dB selected antenna >20dBm> nonselected ATCRBS/Mode S all-call, all-call address _____________ _____________ verify correct all-call address is reported ATCRBS-only all-call interrogation ○ pass ○ fail ○ pass ○ fail verify no reply MTL difference (modeA-modeC) dBm dBm ±1 dBm Squitter ○ pass ○ fail ○ pass ○ fail approx. once/second Auto Test (if available) ○ pass ○ fail ○ pass ○ fail * Ident ○ pass ○ fail ○ pass ○ fail on for ca. 20 seconds * Pilots Code ○ pass ○ fail ○ pass ○ fail * Altitude Code ○ pass ○ fail ○ pass ○ fail see main altimeter at 1013 mb ** Mode S formats ○ pass ○ fail ○ pass ○ fail refer to pages 2 to 4 * No FAR 43 Appendix F requirement. ** Fill in table on page 2/4 Mode S uplink formats 0, 4, 5, 11, 16, 17, 20, 21, 24 Check for which uplinkformats transponder is equipped Check for correct reply, refer to attached downlink format table #1 #2 DF =0 DF =17 DF =0 DF =17 VS =__________ CA =__________ VS =__________ CA =__________ CC =__________ AA =__________ CC =__________ AA =__________ SL =__________ ME =__________ SL =__________ ME =__________ RI =__________ PI =__________ RI =__________ PI =__________ AC =__________ AC =__________ Address =__________ DF =20 Address =__________ DF =20 FS =__________ FS =__________ DF =4 DR =__________ DF =4 DR =__________ FS =__________ UM =__________ FS =__________ UM =__________ DR =__________ AC =__________ DR =__________ AC =__________ UM =__________ MB =__________ UM =__________ MB =__________ AC =__________ Address =__________ AC =__________ Address =__________ Address =__________ Address =__________ DF =21 DF =21 DF =5 FS =__________ DF =5 FS =__________ FS =__________ DR =__________ FS =__________ DR =__________ DR =__________ UM =__________ DR =__________ UM =__________ UM =__________ ID =__________ UM =__________ ID =__________ ID =__________ MB =__________ ID =__________ MB =__________ Address =__________ Address =__________ Address =__________ Address =__________ DF =11 DF =24 DF =11 DF =24 CA =__________ KE =__________ CA =__________ KE =__________ AA =__________ ND =__________ AA =__________ ND =__________ PI =__________ MD =__________ PI =__________ MD =__________ Address =__________ Address =__________ DF =16 DF =16 VS =__________ VS =__________ SL =__________ SL =__________ RI =__________ RI =__________ AC =__________ AC =__________ MV =__________ MV =__________ Address =__________ Address =__________ All tests where performed in accordance with ACG-LTH 40, all limits according to FAR 43 Appendix F. The Transponder(s) are in a airworthy condition. yes no Date and Location Performed by Mode S formats and field contents Downlink Formats FORMAT NO. DF CONTENTS DESCRIPTION 0 0 0000 VS, CC, SL, RI, AC, AP Short Air - Air Surveillance 4 0 0100 FS, DR, UM, AC, AP Surveillance, Altitude Reply 5 0 0101 FS, DR, UM, ID, AP Surveillance, Identity Reply 11 0 1011 CA, AA, PI All Call Reply/Squitter 16 1 0000 VS, SL, RI, AC, MV, AP Long Air - Air Surveillance 17 1 0001 CA, AA, ME, PI Extended Squitter 20 1 0100 FS, DR, UM, AC, MB, AP Comm-B, Altitude Reply 21 1 0101 FS, DR, UM, ID, MB, AP Comm-B, Identity Reply 24 1 1xxx KE, ND, MD, AP Comm-D (ELM) Field contents Field Bits Contents AA 24 The aircraft address announced in the clear, used in DF: 11, 17 AC 13 The altitude code, used in DF: 0, 4, 16, 20. All bits are Zeros if altitude information is not available. Contains metric altitude if M-Bit (26) is One. AP 24 Parity overlaid on the address appears at the end of all transmissions up- and downlink except DF: 11 CA 3 Squitter or All Call Reply, to report Transponder Capability. Codes 4-7 are for squitter only. Used DF: 11 0 Level 1, no communication capability (survaillance only), XPDR transmits DF: 0, 4, 5, 11 1 Level 2, Comm-A and Comm-B capability, XPDR transmits DF: 0, 4, 5, 11, 20, 21 2 Level 3, Comm-A, Comm-B and uplink ELM capability, XPDR transmits DF: 0, 4, 5, 11, 20, 21, 24 3 Level 4, Comm-A, Comm-B up- and downlink ELM capability, transmits DF: 0, 4, 5, 11, 20, 21, 24 4 Level 2, 3 or 4; ability to set code 7 and is on ground 5 Level 2, 3 or 4; ability to set code 7 and is on airborne 6 Level 2, 3 or 4; ability to set code 7 7 DR≠0 or FS=3, 4 or 5 CC 1 Indicates XPDR has ability to support crosslink capability, used in DF: 0 DF 5 The first field in all downlink formats is the transmission descriptor. DR 5 Requests extraction of downlink and appears in DF: 4, 5, 20, 21; codes 1-15 take priority over 16-31 0 No downlink request. 1 Request to send Comm-B message (B-Bit set). 2 TCAS information available. 3 TCAS information available and request to send Comm-B message. 4 Comm-B broadcast #1 available. 5 Comm-B broadcast #2 available. 6 TCAS information and Comm-B broadcast #1 available. 7 TCAS information and Comm-B broadcast #2 available. 8-15 Not assigned. 16-31 Request to send n-segments signified by 15+n. FS 3 Reports flight status of A/C and is used in DF: 4, 5, 20, 21 Code Alert SPI airborne on GND 0 no no yes no 1 no no no yes 2 yes no yes no 3 yes no no yes 4 yes yes either 5 no yes either 6,7 Not assigned ID 13 The 4096 identification code as set by the pilot in DF: 5, 21 Field Bits Contents KE 1 Defines the content of the ND and MD fields in Comm-D replies, DF:24. MB 56 Messages to be transmitted to the interrogator, part of the Comm-B replies, DF: 20, 21. Contains Data Link, Capability reports or A/C Identification Reports or TCAS Resolution Advisory Reports. MD 80 Comm-D field, part of DF: 24, contains one segment of a sequence transmitted by XPDR in the ELM mode. ME 56 Extended squitter message, part of DF: 17, contains broadcast messages. MV 56 Part of the long air-air surveillance reply, DF: 16, contains information used in air-air exchanges (Coordination Reply Messages) ND 4 Provides the segment number transmitted in a downlink ELM and is part of a Comm-D reply, DF: 24 PI 24 Contains the parity overlaid on the interrogator identity code, DF: 11, Mode S Only All Call. RI 4 Information in DF: 0, 16 0 No on-board TCAS. 1 Not assigned. 2 On-board TCAS with resolution capability inhibited. 3 On-board TCAS with vertical-only resolution capability. 4 On-board TCAS with vertical and horizontal resolution capability. 5-7 Not assigned. 8 No maximum airspeed data available. 9 Airspeed is ≤75kts. 10 Airspeed is >75kts and ≤150kts. 11 Airspeed is >150kts and ≤300kts. 12 Airspeed is >300kts and ≤600kts. 13 Airspeed is >600kts and ≤1200kts. 14 Airspeed is >1200kts. 15 Not assigned. SL 3 Reports the current operating sensitivity level of TCAS, is part of air-air surveillance replies, DF: 0, 16 Has no meaning for A/C with RI=0 ( no on board capability to generate resolution advisories). 0 No TCAS sensitivity level reported 1 TCAS operates at sensitivity level 1. 2 TCAS operates at sensitivity level 2. 3 TCAS operates at sensitivity level 3. 4 TCAS operates at sensitivity level 4. 5 TCAS operates at sensitivity level 5. 6 TCAS operates at sensitivity level 6. 7 TCAS operates at sensitivity level 7. 6 Contains XPDR status readouts in DF: 4, 5, 20, 21. VS 1 Indicates A/C is airborne when Zero or on ground when One. |